## Slide 1: Electrical Plan
Tuguss 4 April 2023
Rev 2

## Slide 2
A
B

## Slide 3
Sensor pallet 4 pcs
Sensor Cylinder 7*2=14 pcs
Main Panel
Cylinder 7 pcs
PB Start MC man 1 pcs
JB B
Sensor Cylinder 9*2=18 pcs
JB A
Sub Panel
Sensor pallet 4 pcs
Cylinder 9 pcs
Main Panel
EMG 1 pcs
PB Step 1 pcs
PB Start MC man 1 pcs
EMG 1 pcs
PB Step 1 pcs
Junction B
24V =1
0V =1
I = 21
Q: 7
EMG = 2
Qty Wire: 34
Sub JB1:
1.24V
2.0V
3.I:6
Qty Wire: 8
1
2
3
4
Sub JB2:
1.24V
2.0V
3.I:4
4.EMG: 2
Qty Wire: 8
Sub JB3:
1.24V
2.0V
3.I:4
Qty Wire: 6
Sub JB4:
1.24V
2.0V
3.I:4
Qty Wire: 6
Junction A
24V =1
0V =1
I =25
Q: 8
EMG = 2
Qty Wire: 39
Sub JB5:
1.24V
2.Q:7
Qty Wire: 8
Sub JB1:
1.24V
2.Q:7
Qty Wire: 8
Sub JB2: (1+2)
1.24V
2.0V
3.I:11
4.EMG: 2
Qty Wire: 15
Sub JB3(3+4)
1.24V
2.0V
3.I:12
Qty Wire: 14
opt2
opt3B
opt1
Main Panel
Disable 2 (I)
PL ALARM 1(Q)
Motor 1(Q)
RUNA, RUNB 2(Q)
Selector Sw 2(I)
Buzer
Total I : 21+26+7=54
Total Q : 7 + 8 + 5 = 20
A
B
Sensor pallet base mc 1 pcs
Sensor pallet base mc 1 pcs
I: 1+1+4+14+1 =21
Q:7
IO = 28
Power = 4
EMG = 2
I: 1+1+4+18+1 =25
Q:8
IO : 33
Power : 4
EMG : 2
PB Start 1
PB Stop 1
SS 2 pos 2
SS 3 Pos 1
EMG State 1
Buzer 1
Error 1
PL RUN A 1
PL RUN B 1
RL Motor 1
39
34
Sub JB1:
1.24V
2.Q:8
Qty Wire: 9
Sub JB2: (2)
1.24V
2.0V
3.I:4
4.EMG: 2
Qty Wire: 8
Sub JB3(3+4)
1.24V
2.0V
3.I:12
Qty Wire: 14
opt3A
Sub JB4: (1)
1.24V
2.0V
3.I:9
Qty Wire: 11
Multicore 42x0.5 = 5m
Multicore 16x0.5 = 20m
Multicore 10x0.5 = 20m

## Slide 4
Electrical Distribution
PLC
IO Distribution JB A
IO Distribution JB B
ELCB
MCB
Power Supply 24V
Relay Emergency
Relay Motor
PSU
PLC
MOTOR
MAIN PANEL
SUB PANEL
JB B1 SOLENOID VALVE BLOK
JB B2
JB B3
JB A1
SOLENOID VALVE BLOK
JB A2
JB A3
Option 3 Distribution Electrical Main Panel to Target Objek (Sensor, PB,SV)
Multicore
42x0.5mm
Multicore
16x0.5mm
Multicore
16x0.5mm
Multicore
10x0.5mm
Multicore
10x0.5mm
Sensor
Sensor
Kabel sensor bawaan sensor
Speed Control motor
Motor Conv.
Sensor
Sensor
Kabel sensor bawaan sensor
Sensor
SV
Relay Motor
Relay Emg
JB A4
Sensor

## Slide 5
Electrical Distribution
PLC
IO Distribution JB A
IO Distribution JB B
ELCB
MCB
Power Supply
Relay Emergency
Relay Motor
PSU
PLC
MOTOR
MAIN PANEL
JB B1 SOLENOID VALVE BLOK
JB B2
JB B3
Option 3 Distribution Main Panel
Multicore
16x0.5mm
Multicore
10x0.5mm
Sensor
Sensor
Kabel sensor bawaan sensor
Speed Control motor
Motor Conv.
SUB PANEL
Multicore
42x0.5mm

## Slide 6
Electrical Distribution
PLC
IO Distribution JB A
IO Distribution JB B
MAIN PANEL
SUB PANEL
JB A1
SOLENOID VALVE BLOK
JB A2
JB A3
Option 3 Distribution Sub Panel
Multicore
42x0.5mm
Multicore
16x0.5mm
Multicore
10x0.5mm
Sensor
Sensor
Kabel sensor
bawaan sensor
Kabel sensor
bawaan sensor
JB A4
Sensor

## Slide 7
MAIN PANEL
Option 3
Emg
A
B
EN DIS
EN DIS
MAN SEMI_AUOT FULL_AUTO
MODE
START
STOP
ERROR
ERROR
BUZZER
24V
RUN
RUN
List:
PL Putih 220V
PL Biru 24V
PL Merah 24V
Buz 24V
EMG 3x
PL Hijau 24V 2x
PB Hijau
PB Merah
PB Hitam 2x
SS 2 Pos 2x
SS 3 Pos 3x
Emg
Emg
24V
SUB PANEL
220V
24V
A
RUN
B
RUN
BUZZER

## Slide 8: Design Layout main Panel & Sub Panel
Sub panel
Main Panel
Main panel
Electrical Distribution
PLC
IO+Power Distribution JB A
IO+Power Distribution JB B
IO Distribution JB A
Power Distribution JB A

## Slide 9: Design JB
Multicore
Sensor 1
Multicore
Sensor 2
Sensor 3
Sensor x
Molex 3P M
Box Plastik hitam/PVC cream
Inspirasi
Molex 3P F
SIDE
TOP

## Slide 10: Design JB
Multicore
Sensor 1
Multicore
Sensor 2
Sensor 3
Sensor x
Molex 3P M
Box Plastik hitam/PVC cream
Inspirasi
Molex 3P F
SIDE
TOP

## Slide 11
Group A
S_ph 1
S_ph 2
S_ph 3
S_ph 4
S_ph 5
JB A4
S_Cyl 1
S_Cyl 2
S_Cyl 3
S_Cyl 4
S_Cyl 5
JB A2
S_Cyl 6
S_Cyl 7
PB inc,mc
PB EMG
S Cyl 8
Sub Panel
Main Panel
42x0.5
Group B
S_ph 1
S_ph 2
S_ph 3
S_ph 4
S_ph 5
JB B4
S_Cyl 1
S_Cyl 2
S_Cyl 3
S_Cyl 4
S_Cyl 5
JB B2
S_Cyl 6
S_Cyl 7
PB inc,mc
PB EMG
S Cyl 8
JB B1
SV 1
SV 2
SV 3
SV 4
SV 5
SV 6
SV 7
JB A1
SV 1
SV 2
SV 3
SV 4
SV 5
SV 6
SV 7
INPUT A
Photo sensor 5 pcs
Sensor Cylinder 18 pcs
PB Step: 1 pcs
PB ON mc: 1 pcs
21 pcs
OUTPUT A
Cylinder 8 pcs
INPUT B
Photo sensor 5 pcs
Sensor Cylinder 14 pcs
PB Step: 1 pcs
PB ON mc: 1 pcs
8 pcs
OUTPUT B
Cylinder 7 pcs
7 pcs
25 pcs
OUTPUT C
Buz 1 pcs
PL 3 pcs
RL Motor
5 pcs
INPUT C
SS 4 pcs
PB 2 pcs
State EMG
7 pcs
TOTAL INPUT : 25 + 21 + 7 = 53 PCS
TOTAL OUPTUT : 8 + 7 + 5 = 20 PCS
JB A3
JB A3
8x0.5
8x0.5
10x0.5
10x0.5
8x0.5
8x0.5
10x0.5
10x0.5

## Slide 12
Jual Kabel Control Multicore YSLY-JZ 8x0.5mm Meteran Potongan - Jakarta Barat - JayaMandiriElectric | Tokopedia
Jual Kabel Control Multicore YSLY-JZ 42x0.5mm Meteran Potongan - Jakarta Barat - JayaMandiriElectric | Tokopedia
5m
20m
20m
Jual Kabel Control Multicore YSLY-JZ 10x0.5mm Meteran Potongan - Jakarta Barat - JayaMandiriElectric | Tokopedia

## Slide 14
Plug 220V
ELCB
MCB
PSU
Speed Control Motor
PLC
MCB
MCB
Motor
Terminal Distribution A,B
I
Q
Comm Q Relay EMG
R EMG
PSU 24V
PB EMG 1
PB EMG 1
PB EMG 1
Common Q PLC
PSU

## Slide 15: Time line
TODAY

## Slide 16: Layout depan panel
Main Panel
Sub Panel
JB1
JB2
JB3
Plan:
1. Panel, sub panel, JB dipersiapkan di Tuguss
2. Kebutuhan item 1 disiapkan dalam minggu ini
Main Panel
Panel 600x400
Wire duct 32x45
Wire 1.5 coklat, biru, kuning-hijau
Wire AWG24 coklat, hitam, kuning, biru
Skun
Terminal Blok
DinRail
Plug 220V
ELCB
MCB
PSU
Motor Driver
PLC
PL220VAC putih
Pl24VDC biru
Buzer24VDC
PL24VDC merah
EMG button
PL 24VDC hijau 2X
PB NO Hijau
PB NC Merah
SS 2 Pos 2x
SS 3 pos
Sub Panel
Panel 400x300
Wire duct 32x45
Wire 1.5 coklat, biru, kuning-hijau
Wire AWG24 coklat, hitam, kuning, biru
Skun
Terminal Blok
DinRail
Pl24VDC biru
Buzer24VDC
PL24VDC merah
PL 24VDC hijau 2X
JB
Box JB1 2x
Box JB2 2x
Box JB3 2x
Box JB4 2x
Molex 3 pin
Molex 4 pin
Molex 2 pin
JB3
Box Button Control Machine
BOX button isi 3 lubang 22mm 2x
EMG SW 2x
PB NO Hitam 2x
PB NO Kuning 2x
Installation
Multicore 42x0.5 5m
Multicore 1

## Slide 17: PLC Software
KV Studio
KV Studio Version 11 Update
Version 11 Manual Set